Project 2018 7/30

Description: Space Mouse used to easily rotate Fusion 360 drawings.
Using rotate module, Adafruit Feather M4 , and circuitpython

Components:

1. TSW 7 function scroll whell module from Tindie
2. Adafruit Feather M4
3. MU IDE

Steps:

1. Connect rotatory encoder to Feather:
1.1 Rotary out puts pins D10 , D9
1.2 Rotary buttons , only used two. D11 , D12 pins

2. Develop python code using MU IDE.
2.1 Basic rotatory code
2.2 Space mouse code

3. Test:
3.0 Connect, device should connect as USB mouse
3. 1 Place cursor on screen observe movement using X,Y rotate buttons and rotary wheel
3.2 Fusion 360 , try to precisely rotate drawings

4. 3D print case , using Feather case design with modifications

5. Rotary Test Code

# Rotary Encoder 07/30/2018
# TSWB 7 function Tact and Scroll Wheel
#
# Rating: 1 ma , 10 VDC
# Determines position change +/- 1 for use to move mouse
import time
import board
import digitalio
import rotaryio
class Button():
   def __init__(self, pin, _active_value):
       self.button = digitalio.DigitalInOut(pin)
       self.button.direction = digitalio.Direction.INPUT
       self.button.pull = digitalio.Pull.UP
       self.active_value = _active_value
       self.state = 'NOT_PRESSED'
   def update(self):
       just_pressed = False
       if self.button.value == self.active_value and self.state == 'NOT_PRESSED':
        self.state = 'PRESSED'
        just_pressed = True
       elif self.button.value != self.active_value and self.state == 'PRESSED':
        self.state = 'NOT_PRESSED'
       else:
        pass
       return just_pressed
# LED
led = digitalio.DigitalInOut(board.D13)
led.direction = digitalio.Direction.OUTPUT
led.value = False
# RotaryIO , using pins D10 , D9
encoder = rotaryio.IncrementalEncoder(board.D10, board.D9)
# Rotary Encoder Module buttons
# Pins board.D11 , board.D12
x_rot_button = Button(board.D11,0)
y_rot_button = Button(board.D12,0)
position_change = 0
last_position = encoder.position
while True:
   led.value = False
   if x_rot_button.update():
       print('X_ROT Pressed')
   if y_rot_button.update():
       print('Y_ROT Pressed')
   position = encoder.position
   if position != last_position:
       position_change = position - last_position
       print(position_change)
       last_position = position
   led.value = True

6. Fusion 360 Space Mouse

# Fusion 360 3D Control 07/31/2018
# Rotate Control
# Rotate X
# 1. Press KBD shift
# 2. Press middle mouse button
# 3. Move mouse along X axis
# Rotate Y
# 1. Press KBD shift
# 2. Press middle mouse button
# 3. Move mouse along y axis
#
# Notes:
# Neopixel:
# Power 3.3 V , Connected to pin 8 , CircuitPython pin name is board.NEOPIXEL
import time
import board
import digitalio
import rotaryio
from adafruit_hid.keyboard import Keyboard
from adafruit_hid.keycode import Keycode
from adafruit_hid.mouse import Mouse
import neopixel
class Button():
   def __init__(self, pin, _active_value):
       self.button = digitalio.DigitalInOut(pin)
       self.button.direction = digitalio.Direction.INPUT
       self.button.pull = digitalio.Pull.UP
       self.active_value = _active_value
       self.state = 'NOT_PRESSED'
   def update(self):
       just_pressed = False
       if self.button.value == self.active_value and self.state == 'NOT_PRESSED':
        self.state = 'PRESSED'
        just_pressed = True
       elif self.button.value != self.active_value and self.state == 'PRESSED':
        self.state = 'NOT_PRESSED'
       else:
        pass
       return just_pressed
# LED
led = digitalio.DigitalInOut(board.D13)
led.direction = digitalio.Direction.OUTPUT
# Neopixel RGB LED
RGB_BLUE = (0,255,0)
RGB_GREEN = (0,0,255)
RGB_OFF = (0,0,0)
rgb_led = neopixel.NeoPixel(board.NEOPIXEL, 1, brightness=.3)
def rgb_led_display(color):
   rgb_led[0] = color
   rgb_led.show()
# RotaryIO , using pins D10 , D9
encoder = rotaryio.IncrementalEncoder(board.D10, board.D9)
last_position = encoder.position
def rot_encode():
   global last_position
   position = encoder.position
   position_change = 0
   if position != last_position:
       position_change = position - last_position
       #print(position_change)
       last_position = position
       #print(position_change)
   return position_change
# Rotary Encoder Module buttons , using pins board.D11 , board.D12
x_rot_button = Button(board.D11,0)
y_rot_button = Button(board.D12,0)
def rot_buttons():
   axis = None
   if x_rot_button.update():
       axis = 'x'
       rgb_led_display(RGB_GREEN)
   if y_rot_button.update():
       axis = 'y'
       rgb_led_display(RGB_BLUE)
   return axis
# Keyboard
kbd = Keyboard()
# Mouse
mouse = Mouse()
rot_ctrl_state = 'DISABLED'
rot_axis = None
def rot_ctrl():
   global rot_ctrl_state
   global rot_axis
   global last_position
   axis = rot_buttons()
   if axis is not None and rot_ctrl_state == 'DISABLED':
       # press SHIFT KEY
       kbd.press(Keycode.LEFT_SHIFT)
       time.sleep(0.02)
       # press MIDDLE Mouse button
       mouse.press(Mouse.MIDDLE_BUTTON)
       time.sleep(0.02)
       rot_ctrl_state = 'ENABLED'
       rot_axis = axis
       last_position = encoder.position
       #print('Enable')
   elif axis is not None and rot_ctrl_state == 'ENABLED':
       # Release all keys
       kbd.release_all()
       mouse.release_all()
       rot_ctrl_state = 'DISABLED'
       rot_axis = None
       rgb_led_display(RGB_OFF)
       time.sleep(0.02)
       #print('Disable')
   else:
       pass
   return rot_ctrl_state,rot_axis
def mouse_ctrl(axis , pc):
   if pc == 0 or axis is None:
      return
   _x = 0
   _y = 0
   _d = 1
   if pc < 0:
       _d = -1
   # Rotary control clockwise mouse moves to right
   if 'x' == axis:
       _x = _d
   # Rotary control clockwise mouse moves to up
   if 'y' == axis:
       _y = -_d
   for _ in range(abs(pc)):
       led.value = True
       time.sleep(0.02)
       mouse.move(_x,_y,0)
       led.value = False
rgb_led_display(RGB_OFF)
while True:
   # Response delay
   time.sleep(0.1)
   # Process rotation enable/disable
   rot_enable , rot_axis = rot_ctrl()
   if 'DISABLED' == rot_enable:
       continue
   # If rotary encoder change , move mouse
   rot_inc = rot_encode()
   mouse_ctrl(rot_axis,rot_inc)

7. Project Review
7.1 Working
7.2 Need heavy base designs